Low Pressure Boiler – VOCABULARY A

| 1 | temperature | measure or degree of hotness or coldness of air or liquids measured by a thermometer |
| --- | --- | --- |
| 2 | Fahrenheit | one of two common temperature scales; water freezes at 32°F; water boils at 212°F |
| 3 | Celsius / centigrade | one of two common temperature scales; water freezes at 0°C; water boils at 100°C |
| 4 | heating surface | the part of the boiler where water is on one side and heat from gases of combustion are on the other side |
| 5 | condensate | steam that has lost its heat and turned back into water |
| 6 | feedwater | water that is treated for use in the boiler |
| 7 | compression tank | allows water to expand in the system |
| 8 | first law of thermodynamics | law of conservation of energy = energy cannot be created or destroyed but can be changed from one form to another |
| 9 | second law of thermodynamics | heat always flows from a material of higher temperature to a material of lower temperature |
| 10 | solid | a substance without an internal cavity that has a definite size and shape |
| 11 | liquid | a substance that flows freely and has a definite volume but no independent shape; liquids are only slightly compressible |
| 12 | gas | a substance that has no definite volume or independent shape that tends to expand indefinitely |

Low Pressure Boiler – VOCABULARY B

| 1 | latent heat | heat identified by a change of state and not temperature change of the substances (example: heat added to ice changes it to water but it stays at 32°F) |
| --- | --- | --- |
| 2 | sensible heat | heat that can be measured by a thermometer or sensed by a person |
| 3 | British thermal unit | amount of heat energy required to raise the temperature of one pound of water 1°F |
| 4 | heat exchange | anything that transfers heat from one substance to another without allowing the materials to mix |
| 5 | conduction | heat transfer that occurs when molecules in a material are heated and the heat is passed from molecule to molecule through the material |
| 6 | convection | heat that occurs when currents circulate between warm and cool regions of a fluid |
| 7 | radiation | heat transfer that occurs as radiant energy |
| 8 | combustion | the rapid union of oxygen with an element or compound that results in the release of heat |
| 9 | perfect combustion | combustion that occurs when fuel is burned using only the theoretical amount of air |
| 10 | complete combustion | combustion that occurs when all fuel is burned using the minimum amount of air above the theoretical amount of air required to burn the fuel |
| 11 | MATT | an easy way to remember complete combustion: mixture, atomization, temperature, time |
| 12 | MATT – mixture | mixture of air and fuel, which must be maintained at the proper ratio at all firing rates; high firing rates burn the maximum amount of fuel and require more air than low firing rates |
| 13 | MATT – atomization | atomization of fuel oil: the breaking up of fuel into small particles to maximize contact of fuel with air for combustion efficiency; atomization is not required with gas or coal |
| 14 | MATT – temperature | the proper temperature of the air, fuel, and furnace must be maintained for complete combustion |
| 15 | MATT – time | time required to achieve complete combustion; for maximum efficiency, the combustion process must be completed before the gases of combustion come in contact with the heating surface |

Low Pressure Boiler – VOCABULARY C – ABBREVIATIONS

| 1 | NOWL | normal operating water level |
| --- | --- | --- |
| 2 | MAWP | maximum allowable working pressure |
| 3 | PSI | pounds per square inch |
| 4 | PSIA | pounds per square inch absolute pressure |
| 5 | lbs/hour | pounds per hour |
| 6 | GPM | gallons per minute |
| 7 | H | hydrogen |
| 8 | C | carbon |
| 9 | O2 | oxygen |
| 10 | CO2 | carbon dioxide |
| 11 | H2O | water |
| 12 | N2 | nitrogen |
| 13 | BHP | boiler horsepower |
| 14 | HRT | horizontal return tubular boiler |
| 15 | OSHA | Occupational Safety and Health Administration |
| 16 | EPA | Environmental Protection Agency |
| 17 | ASME | American Society of Mechanical Engineers |